## Slide 1: Robotics
Lesson 4 – Direct kinematics

## Slide 2: Agenda
Interaction routines for the robot Rob3 in joint angular coordinates
Direct kinematics
Examples
Rob 3 direct kinematics implementation

## Slide 3: Rob3 protocol
Initialize Robot
Move a single axis to a specific angle (degree or radians)
Move all axis to specific angles (degree or radians)
Move one axis to specific angle with given speed in degree or radians per unit_time
Move all axis to specific angles in degree or radians per unit_time

## Slide 4: For axis 1
a/160=d/256
0 degree corresponds to 127 steps
0 steps -> -80 degree
function: Steps -> degree
function: degree -> step
0o
0 steps
127 steps
255 steps
+80o
-80o

## Slide 5: The Rob 3

## Slide 6: The Rob 3

## Slide 7: Working range and speed
Resolution

## Slide 8: Rob 3: Joint 1

## Slide 9: Transformation into steps
Digital value between 0 and 255
Teta_1  [-80,80] o -------> [0,255] steps
Teta_2  [-50,+50] o -------> [0,255]
Teta_3  [0,-100] o -------> [0,255]
Teta_4  [--100,+100] o -------> [0,255]
Teta_5  [-100,+100] o -------> [0,255]
Gripper [0, 60]mm -------> [0,255]
Angular resolution for teta_1 = 160/255 = 0.627o/step
Angular resolution for teta_2 = …

## Slide 10: Conversions of steps to degree: Rob3, axis 1
y= m.x + b
=0.62745
-80=m.0+b <=> b=-80
degree(steps) = 0.62745 × steps - 80
…and now few tests:
degree(0) =-80
degree(127) = 0
degree(255)= 80
Conversions for other axis are similar

## Slide 11: Conversions of degree to steps: Rob3, axis 1
y= m.x + b
=1.59375
127=m.0+b <=> b=127
steps (degree) = 1.59375 × degree + 127
…and now few tests:
steps(0) = 127
Step(80) = 255
Steps(-80) = 0
Conversions for other axis are similar

## Slide 12: Move one axis
int move_one_axis(int axis, double angle)
{
int steps;
If(axis==1)
steps=degree_to_steps_j_1(angle);
// put code to here to verify movement is allowed
//….
//…
move_one_axis(port, axis, angle);
}
void move_one_axis(TCommPort *Cp,int axis,int steps)
{
int tam;
char Buff[20];
char comando[10]={0x8+axis-1,steps,3,0};
Cp->Enviar(comando,3,tam);
printf("\n%s...", Cp->GetMensagem() );
Sleep(200);
Cp->EsperarRecepcao();
Cp->Receber(Buff,2,tam);
printf("\n%s...", Cp->GetMensagem() );
}

## Slide 13: Rob3: move 1 axis with speed (1)

## Slide 14: Rob3: move axis 1 with speed (2)
Each step variation corresponds to
THEREFORE, speed_in_steps = number_of_steps / time =
speed_in_steps = (255-0) / 255*T*10ms = 1 step /T*10ms
speed_in_steps = 100/T steps/second

## Slide 15: Rob3: move axis 1 with speed (3)
Each step variation corresponds to
46o/ sec ---------------------> 73.3 steps/sec [divide 46 by joint’s angular resolution 0.627]
46o ---------------------> takes 1 second + 73.3*delay_T
We have that speed_in_degrees = 46o / (1 sec + 73.3*T*10ms) [T ranges from 0 to 255]
If we need to determine T as a function of a specified speed, we take the inverse
Axis 1
For any axis, we have

## Slide 16: Speed per second to T factor
int speed_to_T(double max_speed, double resolution, double desired_speed)
{
double factor = max_speed/resolution;
int T = 1/factor*( (max_spedd/desired_speed) - 1 );
return (int) T;
}
For any axis, we have

## Slide 17: Testing
T = speed_to_T( 46, 160.0/255.0, 10) // 10o/sec
T = 4.911  5
Therefore, if you wish axis 1 to move at 10o/sec , you should set T=5 as the “time” byte to be used in the move axis with speed command.
int speed_to_T(double max_speed, double resolution, double desired_speed);

## Slide 18: Forward kinematics

## Slide 19: TCP coordinates
Given the characteristics of the robot’s links and joints, how to determine the localization and orientation of the TCP?
TCP (tool center point)

## Slide 20: Kinematic equations
Kinematic equations describe the tool frame relative to the base frame as a function of the joint variables.

## Slide 21: Joint and world coordinates

## Slide 22: Direct Kinematics (1)

## Slide 23: Direct kinematics (2)

## Slide 24: Link connection description
The link offset d and the joint angle  are two parameters that may be used to describe the nature of the connection between neighboring links.

## Slide 25: Kinematic function of a link
The kinematic function of a link is to maintain a fixed relationship between the two joint axes it supports. This relationship can be described with two parameters: the link length, a, and the link twist α.

## Slide 26: Frames attachment
Link frames are attached so that frame {i} is attached rigidly to link i.

## Slide 27: Link-frame attachment procedure
Identify the joint axes and imagine (or draw) infinite lines along them. For steps 2 through 5 below, consider two of these neighboring lines (at axes i and i + 1).
Identify the common perpendicular between them, or point of intersection. At the point of intersection, or at the point where the common perpendicular meets the i th axis, assign the link-frame origin.
Assign the Zi-1 axis pointing along the i th joint axis.
Assign the Xi axis pointing along the common perpendicular, or, if the axes intersect, assign Xi to be normal to the plane containing the two axes.
Assign the Yi axis to complete a right-hand coordinate system.
Assign frame {0} to match frame {1} when the first joint variable is zero. For frame {N}, choose an origin location and XN direction freely, but generally so as to cause as many linkage parameters as possible to become zero. Generally, ZN is the approach axis, YN is for sliding and XN normal to ZN-1.

## Slide 28: Link parameters in terms of the link frames
If the link frames have been attached to the links according to our convention, the following definitions of the link parameters are valid:
ai-1 = the distance from Zi-1 to Zi measured along Xi-1
i-1 = the angle from Zi-1 to Zi measured along Xi-1
di = the distance from Xi-1 to Xi measured along Zi
i = the angle from Xi-1 to Xi measured along Z

## Slide 29: Matrix model

## Slide 30: Denavit-Hartenberg Matrix

## Slide 31: Example STANFORD Robot

## Slide 32: STANFORD’s Joints

## Slide 33: Draw imaginary lines along each joint

## Slide 34: Origin of reference frames
Along the lines imaginary lines

## Slide 35: Attach reference frames according to D-H rules

## Slide 36: DH parameters for STANFORD Robot

## Slide 37
We model end-effector
for ROb3 in posterior slides

## Slide 38: Examples with Robot PUMA

## Slide 39: Example with robot PUMA (2)

## Slide 43: Rob3 (draw imaginary lines)

## Slide 44: Place z-axis
z-1 axis along i-th joint

## Slide 45: Rob3 (x-axis)
Along common perpendicular to between consecutive z-axis (from zi-1 to zi).
If zi-1 to zi intercept, x-axis is assigned to be normal to the plane containing the two axis (zi-1 to zi )
Assign Y-axis to complete the right-hand coordinate frame.

## Slide 46: Rob3 Denavit-Hartenberg
joint | teta_i | alpha_i | a_i | D_
1 | 0 | 90 | 0 | d1
2 | 0 | 0 | a2 | 0
3 | 0 | 0 | a3 | 0
4 | 90 | 90 | 0 | 0
5 | 180 | 0 | 0 | d5

## Slide 47: Rob3 DH equations (edited in Mathematica Software)
Transformation matrixes
orientation
position

## Slide 48: Rob3- DH equations

## Slide 49: Performing some tests

## Slide 50: Rob3 with all joints at 0o

## Slide 51: Roll-pitch-yaw
Be carful with arcTan(y/x)

## Slide 52: More accurate ArcTan function
It provides the true angle considering the quadrant specified by components x and y.
It firstly tests whether x and y are zero, which returns 0, or otherwise it returns ArcTan(x,y).
There is a C++ double atan2(y,x) // order of parameters swapped
You can’t call atan2 directly if x==0 and y==0 (domain error).
Define ArcTan2 in C++, which prevents the error when calling atan2

## Slide 53: Function direct_kinematics for Rob3
//int direct_kinematics(double t1, … [here we ommit variable types]
int direct_kinematics(t1, t2, t3, t4, t5, &x, &y, &z, &roll, &pitch, &yaw){
x = cos(t1)*(a2*cos(t2)+a3*cos(t2+t3)+d5*cos(t2+t3+t4);
//… develop remaining code here
//… a2, a3 and d5 are on the DH table
}

## Slide 54: GUI user interface

## Slide 55: Right click in your solution and create empty project C++

## Slide 56: Right click in your solution and create empty project C++

## Slide 57: In the solution explorer, right click in the new project and select Add/New Item

## Slide 58: Select Visual C++UI -> Windows form and click add

## Slide 59: Click “yes” on this message if it appears

## Slide 60: Put at least a button in your form

## Slide 61: Open the source-code c++ of the just created MyRobotForm.cpp (click on it)

## Slide 62: Add the following lines
#include "MyRobotForm.h"
using namespace System::Windows::Forms;
//[MTAThread]
void main(void) {
Application::EnableVisualStyles();
Application::SetCompatibleTextRenderingDefault(false);
Application::Run(gcnew Rob3GUI::MyRobotForm);
}

## Slide 63: Open project Properties: right-click on the new project

## Slide 64: Goto configuration properties/general /Common language runtime -> Select “Common language Runtime Support /clr”
Don’t click ok yet

## Slide 65: In Linker/Advanced/Entry point: write main
Don’t click ok yet

## Slide 66: In Linker/System/Subsystem, select Windows(/SUBSYSTEM:WINDOWS)
Click ok NOW.

## Slide 67: Add main32.cpp and serial32.cpp to your project

## Slide 68: Start filling your User friendly Interface

## Slide 69: Add a Tcomport object to the robot class

## Slide 70: Put code for buttons events
private: System::Void button2_Click(System::Object^ sender, System::EventArgs^ e) {
Cp->Abrir(L"\\\\.\\com12");
}
private: System::Void button2_Click(System::Object^ sender, System::EventArgs^ e) {
Cp->Abrir(L"\\\\.\\com12");
}
private: System::Void button3_Click(System::Object^ sender, System::EventArgs^ e) {
Cp->Fechar();
}
private: System::Void button1_Click(System::Object^ sender, System::EventArgs^ e) {
void move_one_axis(TCommPort *Cp, int axis, int steps);
int axis = System::Convert::ToInt32(textBox1->Text);
int steps = System::Convert::ToInt32(textBox2->Text);
move_one_axis(Cp, axis, steps); // you have this one already done in main32.cpp
}

## Slide 71: Good Work